## Slide 1: LBG-split for CD-quality audio signals
Michelotto Federico 1218322
September 17, 2021
Multimedia Coding - 2020/2021

## Slide 2: Outline
Goal of the project
Vector Quantization
LBG-split method
Initialization by ‘’splitting’’
The empty cell problem
Results

## Slide 3: What is this project about?

## Slide 4
The goal of this project is to implement a vector quantization technique called LBG-split and apply it to CD-quality audio signals.
LBG stands for Linde, Buzo, Gray, the three scientists that devised this procedure.
Split stands for ‘’splitting’’, a technique used for the initialization of this method.

## Slide 5: Vector Quantization

## Slide 6: Vector Quantization (VQ)
Extension of the scalar quantization.
Instead of quantize individual samples, quantize blocks of samples (vectors).
The idea is to exploit the correlation of the source samples in order to increase the efficiency of the coding system.

## Slide 7: Design of a VQ scheme
Parameters:
R : rate per sample
L : codevectors’s dimension
K : codebook size =
Each codevector is represented by a binary index of bits.
Each codevector has samples.
Given R and L:

## Slide 8: Necessary conditions for optimality (not sufficient)
Nearest Neighbour Condition
  Given the codebook the optimal partition of is the one that minimizes the distances.
Centroid Condition
  Given the partition of : .The codevectors of the optimal codebook are the centroids of the decision regions.
These two conditions do not guarantee convergence to the global optimum.

## Slide 9: LBG-split

## Slide 10: LBG
Extension of the popular Lloyd-Max algorithm used for scalar quantization.
Iterative algorithm that aims at minimizing the MSE (Mean Squared Error) exploiting the necessary conditions for optimality.
Two formulations:
  Based on the knwoledge of probability density function of the source.
  Based on a training set.
In practice (and in this project) the second option is used.

## Slide 11: LBG algorithm
Define an initial codebook.
Compute the partition exploting the nearest neighbour condition.
Compute the new codebook (centroids) exploiting the centroid condition.
Compute the overall distortion:
IF the distortion improved less than certain threshold : STOP
ELSE: goto step 2.
The quality of the solution and the speed of convergence depend considerably from the choice of the initial codebook.
For more details, please refer to [1] and [2].

## Slide 12: Example
Initial centers
Partitioning
Centroids computation
Iteration 1
Iteration 2
…

## Slide 13: Initialization by ‘’splitting’’
Build the optimal codebook of size 1 defining codevector as the mean of all vectors in the training set. Set (current codebook size).
Generate new codevector perturbing the existing ones:
Set
Optimize the new codebook using the LBG algorithm.
IF : STOP
ELSE: goto step 2.
:= ‘’codebook at iteration ’’.
Then .
Distortion can only decrease (or stay the same) from one iteration to the next.

## Slide 14: The empty cell problem
During the LBG procedure, a codevector could have no samples associated to it.
There are two viable options:
Substitute the ‘’empty’’ codevector with a sample of the training set using some policy.
Do not update the codevector (in successive iterations it could be the nearest codevector to some samples).

## Slide 15: Strategy for the empty cell problem
Substitute the ‘’void’’ codevector with the sample that contributes the most to the overall distortion measure.
If there are multiple ‘’void’’ codevectors, apply 1) to the first, and do nothing with the others. This is done in order to avoid extra computation.
The remaining ‘’void’’ codevectors will be replaced using 1) in the successive iterations (this is not true only if it happens that all samples contributes to the distortion less than ).

## Slide 16: Dataset
‘’49mono.wav’’: 23 seconds of a woman speaking in english.
‘’54mono.wav’’: 21 seconds of a man speaking in german.
‘’58mono.wav’’: 16 seconds of “Zapataedo, Op. 23 No. 2, Larry Coryell”.
‘’64mono.wav’’: 31 seconds of “Carmina Burana: O Fortuna (1997-Remaster), Philharmonia Chorus & Philharmonia Orchestra & Riccardo Muti”.
‘’70mono.wav’’: 21 seconds of “Early in the mornin’, Eddie Rabbit”.
Since the sound signals were provided without any description, I used the popular mobile app Shazam to retrieve the name of the songs.

## Slide 17: Results

## Slide 18: Results - 1

## Slide 19: Results - 2

## Slide 20: Results - 3

## Slide 21: Results - comparisons ()

## Slide 22: Results: different training and source data
Note that the audio signal “58mono.wav” is the one with the shortest duration.

## Slide 23: Visual result of the LBG-split technique
Training set “70mono.wav” (L=2)
Final codebook

## Slide 24: Conclusions
Varying the perturbation factor didn’t produce significant variations.
As expected, increasing the rate per symbol R, the SNR increases too.
Increasing the vector dimension L seems to be beneficial.
Recalling that the audio signal “58mono.wav” is the one with the shortest duration, it is curious to note that when using different training and source data (table 5.4):
  It’s codebook was the only to obtain SNR values less than 20 db for all the sources.
  Two different codebooks obtained a better SNR when coding the source “58mono.wav”.

## Slide 25: Bibliography
Y. Linde, A. Buzo, and R. Gray. “An Algorithm for Vector Quantizer Design”. In: IEEE Transactions on Communications 28.1 (1980), pp. 84–95.
K. Sayood. Introduction to Data Compression. The Morgan Kaufmann Series in Multimedia Information and Systems. Elsevier Science, 2017. ISBN: 9780128097052.

## Slide 26: Thank you for the attention!